## Slide 1
Chapter 8
TCP/IP Performance over Optical Networks

## Slide 2: Objectives
Gain an overview of optical networks
Learn transport architectures for carrying TCP/IP traffic over optical networks
Understand specific performance issues when TCP/IP traffic is transported over optical networks
Design optical packet switches which maximize TCP performance

## Slide 3: Contents
Optical networks
Multiprotocol label switching
Optical switching
TCP Performance issues

## Slide 4
Optical Networks

## Slide 5: Evolution of Optical Networks
First optic transmission system in early 70s
Optical switching emerged in last few years
Coherent optical transmission based on DWDM
Optical transparent networks
  No optical to electrical conversion
  All functions performed in optics

## Slide 6: IP over DWDM
Overlay approach
  Low efficiency
  High costs for network management
IP over SONET
  Carrying IP packets directly over SONET
  Without SONET layer (PPP/HDLC)

## Slide 7: IP over DWDM (Cont.)
Optical layer accessible through optical UNI (O-UNI)
Integrated approach
  Integrate IP control plane with the optical control plane
  Functions of optical adaptation layer shifted into higher layers (similar to MPLS)

## Slide 8
MPLS

## Slide 9: MPLS
Connection-oriented (as opposed to IP)
Partition network layer function into two basic components:
  Control: responsible for routing
  Forwarding : responsible for processing packets
Enable high speed processing

## Slide 10: MPS
Integrate MPLS with all-optical networks
LSPs are mapped into wavelengths
Support end-to-end networking of optical channel paths between access points
Creates point-to-point optical channels
  OXCs
  Wavelengths

## Slide 11
Optical
Switching

## Slide 12: Optical Burst Switching
A middle term solution towards all optical packet switching
Establish optical connections
  Optical burst determination
  Routing
  Wavelength assignment
  Resource reservation
  End-to-end connection setup

## Slide 13: Optical Packet Switching
Optimize the exploitation of DWDM channels
Transparent optical packet routers carrying TCP/IP traffic
Minimum electro-optical conversion
  Packet label/header converted from optical to electrical
  Payload is switched optically

## Slide 14
TCP Performance
Issues

## Slide 15: DWDM Optical Router
Fig. 8.3
Functional blocks
  Input-output interfaces
  Optical space switch
  Delay line buffer
  Electronic control

## Slide 16: Congestion Resolution
Queuing
  Time domain
  Achieved by delay lines (coils of fibers)
Wavelength multiplexing
  Wavelength domain
  Wavelength circuit (WC)
  Wavelength packet (WP)

## Slide 17: TCP Performance over Optical Networks
Latency has significant impacts on TCP window evolution
Fixed latency with overlay approach and MPS
Variable latency with optical burst/packet switching

## Slide 18: End-to-End Delay
Consists of three components
  Interface delay
    Packetization delay
    Transmission delay
  Node delay
    Header processing
    Switching matrix setup
    queuing delay in fiber delay lines
  Propagation delay

## Slide 19: Mapping TCP in Optical Packets
Why map TCP in optical packets
  High data rate
  Large bandwidth-delay product
Share an optical pipe among many TCP connections
Fill optical packets with TCP segments

## Slide 20: Optical Packet Design in TCP/IP Environment
Packetization efficiency
  Fig. 8.7
  Optimal value increases as the time-out increases
Packetization Delay
Congestion Window