## Slide 1
Chapter 7
TCP/IP Performance over Mobile Networks

## Slide 2: Objectives
Explain the characteristics of mobile networks
Understand specific issues concerning TCP performance degradation due to mobility
Learn techniques to address TCP performance problems caused by mobility

## Slide 3: Contents
Characteristics of mobile networks
TCP performance in cellular networks
TCP performance in ad hoc networks

## Slide 4
Mobile
Networks

## Slide 5: Characteristics of Mobile Networks
Cellular networks
  Base station (BS) arbitrates channel allocation
  Mobile hosts communicate with each other via BSs
Ad hoc networks
  No BS
  All mobile hosts act as routers
Fig. 7.1

## Slide 6: Cellular vs Ad-hoc Networks

## Slide 7
TCP
Performance in
Cellular Networks

## Slide 8: Mobile IP
Support mobility of Internet users
Entities
  Mobile host (MH)
  Static corresponding host (SH)
  Home agent (HA)
  Foreign agent (FA)

## Slide 9: Mobile IP (Cont.)
Operations
  Forward path
    Visiting mobile host registers with HA
    HA receives packets on behalf of the mobile host
    HA tunnels IP packets to the mobile host
  Reverse path
    The mobile host sends packets directly to the SH

## Slide 10: Mobile IP (Cont.)
Operations
  Triangle routing
  Routing optimization
Fig. 7.2

## Slide 11: Impacts of Mobility on TCP Performance
Blackouts
  Location
  Fading
  Degrade TCP throughput
Handoff latency
  Packet re-routing
  Bursty losses
  Degrade TCP throughput

## Slide 12: Impacts of Mobility on TCP Performance (Cont.)
Triangular routing and large RTT
  Triangular causes extra delay
  TCP throughput inversely proportional to RTT
  Large RTT results lesser throughput

## Slide 13: Approaches to Improve TCP Performance
Wireless TCP (WTCP)
  Rate-based transmission
  Re-transmission timer not used
  Inter-packet separation is used as indication of congestion (as opposed to packet loss)
  Only consider forward path characteristics when performing congestion control
  Allow TCP to ramp up to the available bandwidth in one RTT

## Slide 14: Approaches to Improve TCP Performance (Cont.)
Fast hand-offs
  HA uses multicast address to forward packets
  Packets are automatically forwarded to BS
  The new BS joins the multicast group before hand-off occurs
  The new BS buffers last few packets
  The new BS starts forwarding the buffered packets to the mobile host after hand-off

## Slide 15: Approaches to Improve TCP Performance (Cont.)
End-to-end approach to host mobility
  A mobile host updates DNS with its new address, upon moving into a new network
  Corresponding hosts learn the new address in a seamless manner
  Migrate all TCP connections to the new location of the mobile host

## Slide 16
TCP Performance
in Adhoc Networks

## Slide 17: TCP Performance Issues in Ad Hoc Networks
Route failure
  TCP may lose a congestion window of packets
  Large RTT variation
  Degrade TCP throughput
Route Re-computation
  Incur extra delay
  Result in a more inflated re-transmission time-out

## Slide 18: TCP Performance Issues in Ad Hoc Networks (Cont.)
Network Partition
  TCP may reset the connection if the partition lasts for more than 100 sec.
  TCP enters slow-start phase after cutting down its window size to 1
  Degrade TCP throughput

## Slide 19: Approaches for Improvement
TCP-feedback and TCP-ELFN
  Employ Explicit Link Failure Notification (ELFN)
  A source node issues a route re-computation request upon receipt of an ELFN
  Reset TCP congestion window size to half its size (instead of 1)

## Slide 20: Approaches for Improvement (Cont.)
Hop-by-hop rate control
  Each router (mobile host) performs rate control on each of its outgoing links based on feedback from downstream routers
  Feedback time is minimal
  More responsive to route failures