## Slide 1
Chapter 6
TCP/IP Performance over Wireless Networks

## Slide 2: Objectives
Gain a high-level overview of the most widely used wireless networks
Understand how characteristics of wireless links adversely impact TCP performance
Learn techniques to enhance TCP/IP performance over wireless networks

## Slide 3: Contents
Wireless networks
TCP performance issues over wireless links
Improve TCP performance over wireless links
Evolution of wireless systems

## Slide 4
Wireless
Networks

## Slide 5: Generic characteristics of Wireless Networks
Similar propagation delay as wireline networks
High error rate
  Interference
  Atmospheric condition
  Multipath fading

## Slide 6: Wireless LAN (WLAN)
Wireless link layer
Operate at 900 MHz/2.4 GHz/5 GHz band
Ethernet connectivity to higher layers
  Same header
  Same checksum
  Same frame size

## Slide 7: WLAN (Cont.)
MAC employs CSMA
  No Collision Detection (CD)
  Loss/error recovery left to higher layers
Interconnection with wired networks
  Through a router equipped with both wired and wireless interfaces
  Through a transparent bridge

## Slide 8: Examples of WLAN
Lucent’s WaveLan
  900 MHz or 2.4 GHz
  2 Mbps
  CSMA/CA
IEEE 802.11
  An enhancement over WaveLan
    Optional ACK
    WLAN coordination (master host)
  1 or 2 Mbps

## Slide 9: Examples of WLAN (Cont.)
IEEE 802.11a
  Operate a 5 GHz band
  Bit rate: between 6 and 54 Mbps
IEEE 802.11b
  Operate a 2.4 GHz band
  Bit rate: 5.5/11 Mbps

## Slide 10: Cellular Communications (CC) Networks
First generation (e.g. AMPS)
  Analog
Second generation
  Digital
  Modest bit rate
  Circuit-switched
  Employed TDMA/CDMA for medium control

## Slide 11: CC Networks (Cont.)
Higher transmission and propagation delays, compared with WLAN
FEC added to each frame
Interleaving (of frames) implemented

## Slide 12: CC Networks (Cont.)
Interconnected to other networks using Interworking Function (IWF)
Fig. 6.1

## Slide 13: Examples of CC Systems
GSM
  Data rate: 9.6 Kbps
  240 bits ARQ (selective repeat)
  Variable throughput and delay
IS-136
  Data rate: 9.6 Kbps
  Advanced ARQ (256 bits)

## Slide 14: Examples of CC Systems (Cont.)
IS-95 (CDMA)
  Data rate: 8.6 Kbps
  172 bits ARQ
  Negative ACK
  Trade reliability for limited delay variance

## Slide 15
TCP
Performance over
Wireless

## Slide 16: TCP Performance Issues
Inappropriate reduction of congestion window
  TCP backs off upon detection of packet loss
  Wireless transmission errors not related to network congestion
Severe degradation in TCP throughput

## Slide 17: TCP Performance Issues (Cont.)
Throughput loss
WLAN
  Frame Error Rate (FER)
  22% reduction in WaveLan
CC systems
  Increased processing delay due to interleaving
  Widely varying RTT
  Disruptions caused by link resets

## Slide 18
Improving TCP
Performance

## Slide 19: TCP Enhancement Schemes
Splitting TCP Connections
  Split TCP connections at wireless gateways
  Reduce TCP end-to-end path
  Significant processing overhead

## Slide 20: TCP Enhancement Schemes (cont.)
Snooping TCP at BS
  Better than split TCP
  Confine retransmission to wireless paths only
  Fig. 6.4

## Slide 21: TCP Enhancement Schemes (Cont.)
Notifying the causes of packet loss
  Explicit Loss Notification (ELN)
  Work well together with Snoop TCP
Adding selective ACK to TCP
  SACK
  Combat multiple losses in one RTT

## Slide 22: Comparison
Things need to consider when assess TCP enhancement schemes
  End-to-end semantics
  IP payload access
  Wireless gateway overhead
  Ease of deployment
  Table 6.4

## Slide 23
Evolution of Wireless Systems

## Slide 24: Evolution of Wireless Systems
Trends in CC systems
  Support high bit rate data service
    HSCSD
    GPRS
    EDGE
  Third generation CC systems
    UMTS
    3G

## Slide 25: Trends in WLAN
Provide high speeds
Support mobility between adjacent networks
Develop more efficient MAC protocols
Personal Area Network (PAN)
Bluetooth
LMDS

## Slide 26: TCP/IP over Heterogeneous Wireless Systems
Challenges
  Multiple systems co-exist
  Direct interoperability between different wireless systems
  Hierarchical cellular systems
Research projects
  Multi-Service Link Layer (MSLL)
  Wireless Internet Network (WINE)
  Wireless Adaptation Layer (WAL)