## Slide 1
Chapter 11
New TCP Standards
And Flavors

## Slide 2: Objectives
Compare the variations in congestion congestion control algorithms of different TCP flavors
Learn how network simulation can be used to compare the performance of different TCP flows

## Slide 3: Contents
Fast retransmission and fast recovery
TCP NewReno
Selective Acknowledgement (SACK)
Forward Acknowledgement (FACK)
TCP Vegas
Performance comparison of TCP flavors

## Slide 4
Fast Retransmit
And
Fast Recovery

## Slide 5: Fast Retransmit
Duplicate ACKs (dupacks) trigger retransmission
  Avoid retransmission timeout
Actions performed by the sender upon receiving 3 dupacks:
  Reduce ssthresh to half of cwnd
  Reset cwnd to 1 segment
  Retransmit the lost TCP segment
Implemented in TCP Tahoe

## Slide 6: Fast Recovery
Based on the fact that a duplicate ACK (dupack) indicates that a segment has left the network
Keep track of of the No. of dupacks received
Inflate cwnd by one segment for each dupack received
Come out of fast recovery when receives an ACK for the segment resulting in the duplicate ACKs
Timeout still occurs when there are multiple consecutive loss in a window

## Slide 7
TCP New Reno

## Slide 8: TCP NewReno
Effects of timeout on throughput:
  TCP cannot send data during timeout period
  cwnd is reset to 1 segment
Avoid timeouts in the case of multiple consecutive losses
Upon receipt of a partial ACK:
  Does not come out of fast recovery
  Assume the segment immediately after the most recently ACKed segment has been lost
  Retransmit the lost (assumed) segment

## Slide 9
Selective
Acknowledgment

## Slide 10: TCP SACK
Avoid timeouts in the case of multiple consecutive losses
Inform the sender which segments have been received
  The receiver uses TCP SACK blocks to indicate contiguous blocks of data successfully received
  The sender infers (from the SACK blocks) which segments are missing (holes in Seq. No)
The sender retransmits missing segments without waiting for timeout

## Slide 11
Forward
Acknowledgment

## Slide 12: Forward Acknowledgment (FACK)
Better recovery from multiple consecutive losses
Keep track of the correctly received data with the highest sequence number
TCP maintains 2 additional variables:
  fack: represents the forward-most segment ACKed
  retran_data: reflects the amount of outstanding retransmitted data
Estimate the amount of outstanding data during recovery

## Slide 13
TCP Vegas

## Slide 14: TCP Vegas
Fundamentally different from other TCP variants
Not wait for loss to trigger cwnd reduction
Estimate current throughput every RTT
Compare current throughput with the expected throughput
  Linearly increase cwnd if diff < 2
  Linearly decrease cwnd if diff > 4
Modified slow start
  Find the correct window size without incurring a loss
Modified retransmission
  Retransmit after one duplicate ACK (as opposed to 3 dupacks)

## Slide 15
Comparing TCP
Flavors

## Slide 16: Performance Comparison of TCP Flavors
Network topology used
Fig. 11.3
Compare performance of TCP variants against TCP Reno

## Slide 17: Performance Comparison of TCP Flavors (Cont.)
Goodput
  Table 11.2
Round trip time
  Table 11.3
Time granularity
  Table 11.4