## Slide 1
Chapter 3
Performance Measurement of TCP/IP Networks

## Slide 2: Objectives
Appreciate the role of measurement in building and maintaining high-performance TCP/IP networks
Explain the types of tools available for performance measurement
Familiarize with freely available performance measurement and testing tools
Select an appropriate tool for a given task

## Slide 3: Contents
Why network measurement
Measurement tasks
Classification of measurement tools
Practical measurement tools
Selecting the right tool

## Slide 4
Why Network
Measurement

## Slide 5: Why Network Measurement
Network management
  Monitor performance (e.g. performance bottleneck)
  Improve network services
Network traffic analysis
  Characterize traffic load
  Input for network design

## Slide 6: Why Network Measurement (Cont.)
Network research
  Collect packet traces
Traffic modeling
  Validate TCP model
Protocol implementation
  Inspect packet header
  Identify packet payload
  Debug

## Slide 7
Measurement
Tasks

## Slide 8: Measurement Tasks
Data collection: Collect raw data from operational network
Analysis: Obtain traffic characteristics (e.g. avg. throughput, delay, etc.)
Presentation: Visualize network performance
Interpretation: Ultimate goal of measurement tasks

## Slide 9
Tool
Classification

## Slide 10: Classification of Measurement Tools
Depending on purposes of measurement
  Monitoring tools (e.g. Tcpdump, tcpstat)
  Benchmarking tools (e.g. ttcp, NetPerf, etc.)
  Fig 3.1

## Slide 11: Classification of Measurement Tools (Cont.)
Depending on level of tasks
  Collector
  Analyzer
Depending on implementation
  Software tools
  Hardware tools

## Slide 12
Measurement
Tools

## Slide 13: Practical Measurement Tools
Tcpdump
Tcpstat
Netperf
NetPIPE
DBS (Distributed Benchmark System

## Slide 14: Tcpdump
Capture header/payload information
Implemented on Unix platform
libpcap: Capture and filter packets
tcpdump: Analyze packet structure

## Slide 15: Tcpstat
Report TCP related statistics periodically
  Bandwidth used
  No. of packets exchanged
  Avg packet size
libpcap: Capture and filter packets
tcpstat: Count packets
Invoked with superuser privilege

## Slide 16: Ttcp
Measure TCP throughput
  TCP
  UDP
Installation

## Slide 17: Netperf
Active testing tool (benchmarking)
Measure available bandwidth between two nodes
Major features:
  Generate different traffic patterns
    Bulk data transfer (e.g. FTP)
    Interactive data exchange (e.g. rlogin)
  Detailed and precise measurement
  Besides TCP/UDP, also support datalink and other network protocols

## Slide 18: Netperf (Cont.)
Fig. 3.15

## Slide 19: NetPIPE
Benchmarking tool
Application-oriented
  Determine optimal message size
  Observe congestion level with a particular message size
Protocols supported:
  TCP
  MPI
  RPC
  AAL5

## Slide 20: NetPIPE (Cont.)
Fig. 3.17

## Slide 21: DBS (Distributed Benchmark System)
Measure performance of multiple TCP connections in parallel
Support sophisticated test traffic patterns
Evaluation of other important aspects of TCP
  Retransmission control
  Congestion avoidance control
Usage

## Slide 22: DBS (Cont.)
Fig. 3.20

## Slide 23: Comparison
Table 3.9
All six tools are compared against 10 different features

## Slide 24
Selecting Right Tool

## Slide 25: Selecting the Right Tool
Things need to be considered
  Measurement capability
  Platform supported
  Measurement objective
  Availability
Refer to Tables 3.9 and 3.10