## Slide 1
Chapter 5
TCP Modeling

## Slide 2: Objectives
Appreciate mathematical modeling of TCP for performance optimization of TCP/IP networks
Understand the fundamental relationship between packet loss probability and TCP performance
Apply a range of mathematical models to predict TCP performance

## Slide 3: Contents
Motivation
Essentials of TCP modeling
TCP models

## Slide 4
Motivation

## Slide 5: Motivation for TCP Modeling
TCP operating scale is very large
  Models are required to gain deeper understanding of TCP dynamics
Uncertainties can be modeled as stochastic processes
Drive the design of TCP-friendly algorithms for multimedia applications
Optimize TCP performance

## Slide 6
Essentials of
TCP Modeling

## Slide 7: TCP Modeling Essentials
Mainly Reno flavors are modeled
Two main features are modeled
  Window dynamics
  Packet loss process

## Slide 8: Window Dynamics
Linear increase and multiplicative decrease is modeled
The standard assumption
  X(t) = W(t)/RTT

## Slide 9: Packet Loss Process
Packet loss triggers window decrease
Packet loss is uncertain
This uncertainty is typically modeled as a stochastic process
  E.g. probability p of losing a packet

## Slide 10
TCP Models

## Slide 11: Gallery of TCP Models
Periodic model
Detailed packet loss model
Stochastic model
Control system model
Network system model

## Slide 12: Periodic Model
Simplest model for TCP
  No specific flavor assumed
Assumes a periodic pattern of congestion window
  See Fig 5.1
X(p) = (1/RTT)*Root(3/2p)
  P is the packet loss probability

## Slide 13: Example 1 - Question
If a TCP connection has an average RTT of 200ms, and packet loss probability 0.05, what is the average throughput?

## Slide 14: Example 1 - Answer
RTT=0.2, p=0.05.
Using Eq. (5.4), throughput is obtained as:
X=(1/0.2)*(root(3/2x0.05)) = 27.4 pkts/sec