## Slide 1
Chapter 9
TCP/IP Performance over Satellite Networks

## Slide 2: Objectives
Appreciate the role of satellites in TCP/IP networks
Gain insight into the fundamental satellite link characteristics affecting TCP performance
Expose to a wide variety of approaches to address TCP performance issues in satellite networks
Select appropriate tools and techniques to improve TCP/IP performance over satellite networks

## Slide 3: Contents
Satellites
Characteristics affecting TCP
TCP performance enhancements for satellite networks

## Slide 4
Satellites

## Slide 5: Brief History
First satellite network accessing the Internet (SATNET) initiated in mid 1975
Four ground stations connected by a simplex 64 Kbps channel
New generation satellite networks being developed to support Internet access and multimedia

## Slide 6: Types of Satellites
Space segment
  Geostationary orbit (GEO)
  Non-Geostationary orbit (NGEO)
    Medium Earth Orbit (MEO)
    Low Earth Orbit (LEO)
Ground segment

## Slide 7: Motivations for Using Satellites in TCP/IP Networks
Ubiquitous coverage
Bandwidth flexibility
Cost-effective
Easy Deployment
Reliability and security
Disaster recovery
Connectivity

## Slide 8: Satellite Internet Architecture
Satellite Internet can be classified into two major categories:
Connectivity networks
  Avoid some degree of ground infrastructure
Access networks
  Interactive connectivity to the Internet
  Highly asymmetric links
  Frequency reuse

## Slide 9
Characteristics
Affecting TCP

## Slide 10: Satellite Characteristics Affecting TCP
Long feedback loop
  Table 9.4
  Impacts on TCP
    Slow start
    Congestion avoidance
    Fast retransmit and fast recovery
    TCP fairness

## Slide 11: Satellite Characteristics Affecting TCP (Cont.)
Link impairment
  Multipath fading
  Interference
  Rain attenuation
  Shadowing
  Negative impacts on TCP throughput
    Fig. 9.5

## Slide 12: Satellite Characteristics Affecting TCP (Cont.)
Bandwidth-delay product
  Large BDP limits TCP throughput
  Table 9.5
  Instability of TCP congestion control
Bandwidth asymmetry
  Low bandwidth ACK path
  Slow down the growth of TCP sender window during Slow Start

## Slide 13: Satellite Characteristics Affecting TCP (Cont.)
Variable delays
LEO handoff
Spectral congestion
Security

## Slide 14
TCP Enhancements

## Slide 15: TCP Enhancements for Satellite Networks
Path MTU discovery
  Enable a sender to find out the maximum possible TCP segment size
TCP for transactions
  Reduce handshaking latency
  From 2 RTT to 1 RTT
Window scaling

## Slide 16: TCP Enhancements for Satellite Networks (Cont.)
Large initial window
Byte counting
Delayed ACKs after Slow Start
Explicit Congestion Notification (ECN)
Multiple connections
Pacing TCP segments
Header compression

## Slide 17: Advanced TCP Enhancements for Satellite Networks
Quick-Start TCP
High-speed TCP
TCP Peach
Explicit Transport Error Notification (ETEN)
TCP Westwood
XCP

## Slide 18: Advanced TCP Enhancements for Satellite Networks (Cont.)
New transport protocol for satellite links
  Designed specifically for satellite environments
  Satellite Transport Protocol (STP)
  Space Communications Protocol Specifications-Transport Protocol (SCPS-TP)
Performance Enhancement Proxy (PEP)

## Slide 19: Performance Enhancement Proxy (PEP)
Typically implemented at transport or application layer
Mitigate problems of TCP over satellite links
Examples of PEP
  Transport layer
    TCP spoofing
    TCP splitting

## Slide 20: PEP (Cont.)
Examples of PEP (Cont.)
  Application layer
    Web cache
    Relay Mail Transfer Agent
PEP mechanisms
Many PEPs use TCP ACK manipulation
  Local retransmissions (e.g. Snoop)
  TCP ACKs filtering and reconstruction

## Slide 21: PEP Mechanisms
Support compression
Handle link discontinuities or link outages
Implications of using PEPs
  Fate sharing
  End-to-end reliability
  End-to-end Diagnostics
Security with PEPs