## Slide 1
Chapter 2
TCP/IP Fundamentals

## Slide 2: Objectives
Gain an understanding of the basic services provided by TCP, UDP and IP
Explain the congestion control algorithms employed by TCP
Describe protocol details of TCP needed to ensure reliable transfer over unreliable networks

## Slide 3: Contents
TCP services and protocols
UDP services and protocols
IP services and protocols

## Slide 4
TCP

## Slide 5: TCP Services
Connection-oriented
Streaming
Full-duplex
Reliable
End-to-end semantic

## Slide 6: TCP Header Format
Fig. 2.1

## Slide 7: TCP Header Format (Cont.)
Source Port (16 bits)
Destination Port (16 bits)
Sequence number (32 bits)
Ack number (32 bits)
Header Length (4 bits)
Reserved (6 bits)

## Slide 8: TCP Header Format (Cont.)
Flags (6 bits)
Receiver window size (16 bits)
Checksum (16 bits)
Urgent Pointer (16 bits)
Options (variable)
TCP Header is 20 bytes long (without options).

## Slide 9: Encapsulation in IP
Fig. 2.2

## Slide 10: Acknowledgement Mechanism
Cumulative ACK
ACK-only segment and Piggybacking
Delayed ACK
Duplicate ACK

## Slide 11: Retransmission Mechanism
Retransmission timer
Estimation of RTT
Granularity of RTO
  Typically 1 sec.
  Smaller value used in some implementations (e.g. Solaris)

## Slide 12: Flow Control
Prevent buffer overflow at TCP receiver
Regulate sending rate at TCP sender
Mechanism
  Sliding window
(p37, Fig. 2.5)

## Slide 13: Congestion Control
Prevent buffer overflow at routers
Regulate sending rate at TCP sender
Mechanism
  Slow-Start
  Congestion Avoidance
  Additive Increase, Multiplicative Decrease (AIMD)

## Slide 14: TCP Slow Start
Start with small window
Increased window by 1 each time ACK rcvd
Window increases exponentially

## Slide 15: TCP Congestion Avoidance
Exponential increase may cause congestion
Force linear increase after a threshold
Linear increase avoids possible congestion

## Slide 16
UDP

## Slide 17: UDP Services
Connectionless
Datagram-oriented
Unreliable
Applications
  Multicasting
  Network management
  Routing Table Update
  Real-time multimedia

## Slide 18: Key Differences Between TCP and UDP
TCP | UDP
Connection-oriented | Connection-less
Stream-oriented | Datagram-oriented
Reliable | Unreliable
Flow-Control | No Flow-Control
Congestion control | No congestion control

## Slide 19: UDP Header Format
Fig 2.8

## Slide 20: UDP Header Format (cont.)
Source port (16 bits)
Destination port (16 bits)
Length (16 bits)
Checksum (16 bits)
UDP Header is only 8 bytes long!

## Slide 21: Encapsulation in IP
UDP packets are encapsulated in IP payload
  Similar to TCP (see Fig 2.2)
First 8 bytes of IP payload contains UDP header

## Slide 22
IP

## Slide 23: IP Services
Provides an unreliable datagram service
IP datagrams may arrive out of order, because different datagrams may take different routes in the network
Datagrams may get lost
Duplicates may be received (if one is retransmitted when the original is still in the network)

## Slide 24: Fragmentation and Reassembly
Intermediate routers may fragment an IP datagram into several IP datagrams
  If it does not fit in the payload of link layer
Fragmentation increases number of bits transmitted for a given TCP segment
Different fragments may travel different paths
If one fragment is lost, entire IP datagram is discarded at the destination

## Slide 25: IP Header
Fig 2.10

## Slide 26: IP Header (cont.)
Version
Header Length
Type of Service
Total Length
Identifier
Flags and Fragment Offset

## Slide 27: IP Header (cont.)
Time to live
Protocol
Header Checksum
Source and Destination Addresses
Options
IP Header is 20 bytes long (without options).