## Slide 1
Chapter 10
TCP/IP Performance over Asymmetric Networks

## Slide 2: Objectives
Explain types of asymmetry that are present in today’s networks
Comprehend specific performance issues when TCP/IP traffic is transported over asymmetric networks
Learn techniques to address TCP performance problems in asymmetric environments

## Slide 3: Contents
Network asymmetry
How asymmetry degrades TCP performance
TCP improvements over asymmetric networks

## Slide 4
Network
Asymmetry

## Slide 5: What is Network Asymmetry?
Network asymmetry refers to the situation where characteristics in the uplink are different than those in the downlink
Examples
  Cable model
  ADSL
  Satellite

## Slide 6: Types of Network Asymmetry
Bandwidth asymmetry
Media-access asymmetry
Loss rate asymmetry

## Slide 7: Bandwidth Asymmetry
Forward and reverse bandwidth are significantly different
Typically downlink bandwidth is 10-1000 times the uplink bandwidth
Example: Direct PC has a 400Kbps downlink and a 56Kbps dialup uplink

## Slide 8: Media-Access Asymmetry
Can occur when transmitter and receiver use shared medium (wired or wireless), and
Transmitter experiences larger (smaller) MAC delay than receiver
Can happen in both cellular and packet radio networks

## Slide 9: Loss-Rate Asymmetry
Packet loss probability in the uplink may be different than that of downlink
This can happen if one of the links is more congested than the other, for example
Loss-rate asymmetry can occur in any network, and it may be a transient phenomenon

## Slide 10
Asymmetry and
TCP Performance

## Slide 11: Impact of Bandwidth Asymmetry
Unidirectional data transfer
  File download from a server
  Normalised bandwidth ratio k determines the behaviour of TCP
  On average, only 1 ACK gets through for every k packets sent
    Increase the chance of data packet loss
    Infrequent ACKs result in slower growth of congestion window
    Loss of ACKs could cause long idle periods
Bidirectional data transfer
  Exacerbate the problem due to bandwidth asymmetry
    Interaction between data packets of the upstream transfer and ACKs of the downstream transfer

## Slide 12: Impact of Media-Access Asymmetry
A central base station suffers lower MAC overhead than distributed nodes
MAC overhead makes it expensive to transmit packets in one direction when there is an ongoing data transfer in the opposite direction

## Slide 13: Impact of Media-Access Asymmetry (cont.)
Fig. 10.6

## Slide 14
TCP Improvements

## Slide 15: TCP Performance Enhancements over Asymmetric Networks
Two key issues need to be addressed:
  Manage bandwidth usage on the uplink
    Reduce the number of ACKs
  Avoid adverse impact of infrequent ACKs
Solutions:
  Local link-layer solutions
  End-to-end techniques

## Slide 16: Uplink Bandwidth Management
Can be realised by:
  Control the degree of compression
  Control the frequency
  Control the scheduling of upstream ACKs

## Slide 17: TCP Header Compression
For use over low-bandwidth links running SLIP/PPP
Reduce the size of ACKs on the slow uplink
Some problems remain:
  MAC overhead
    Independent of packet size
  Adverse interaction with large upstream data packets
    Bidirectional traffic

## Slide 18: ACK Filtering (AF)
TCP-aware link-layer technique
Reduce the number of TCP ACKs sent on upstream channel
Router maintains states for connections that have ACKs packets enqueued.
Remove “redundant” ACKs packets
  Duplicate ACKs not removed
  Selective ACKs not removed

## Slide 19: ACK Congestion Control (ACC)
Operate on an end-to-end basis
Apply congestion control to ACK packets
Mimic TCP congestion control mechanism
Employ delayed ACK
  One ACK sent for every d data packets received
  One ACK acknowledges several data packets
Example: RED+ECN

## Slide 20: ACKs-First Scheduling
ACK packets may be delayed by data packets in a FIFO queue
Separate ACK packets from data packets
Give priority to ACKs
  ACK packets are usually small (compared with data packets
  Minimal impacts in data packets
Large data packet still causes delay
  Segment large data packet before transmission

## Slide 21: Handling Infrequent ACKs
Done either end-to-end or locally at the constrained uplink
TCP Sender Adaptation (SA)
End-to-end technique
The number of back-to-back packets can be sent is bounded
Take into account the amount of data (rather than number of packets) received
Mimic the effect of delayed ACK algorithm

## Slide 22: ACK Reconstruction (AR)
Local technique
Reconstruct the ACK stream after it has traversed the upstream direction bottleneck link
Enable implementation of AF or ACC with changes to TCP senders
Deploy a soft-state agent called ACK reconstructor at the upstream end
ACK threshold determines the spacing between interspersed ACKs at the output
TCP senders can increase their cwnd at the right rate
  Avoid burst behaviour

## Slide 23: Experimental Evaluation: Bandwidth Asymmetry
TCP Reno enhanced with ACC, AF, SA and AR
AF/AR and AF/SA have the best performance
  Table 10.1
  15%--21% increase in throughput
Degree of burstiness is significantly reduced
SA/AR is effective in overcoming the burstiness that results from a lossy ACK stream
Random drop is superior to drop-tail

## Slide 24: Experimental Evaluation: Media-Access Asymmetry
Protocols investigated: TCP Reno, Reno with ACC/SA and Reno with AF/SA
AF and ACC with SA yield better performance than Reno
  Fig. 10.8
AF/SA outperforms ACC/SA
Improvement in throughput
  25% for 1 wireless hop
  41% for 3 wireless hops

## Slide 25: Experimental Evaluation: Media-Access Asymmetry (cont.)